## Slide 1: Buffer Bloat! Obesity: it’s not just a human problem…
Fred Baker

## Slide 2: What is buffer bloat? Why do I care?
Best shown using an example…
Ping RTT from a hotel to Cisco overnight
RTT varying from 278 ms to 9286 ms
Delay distribution with odd spikes about
a TCP RTO apart;
Suggests that we actually had more than
one copy of the same segment in queue
Because few applications actually worked

## Slide 3: A typical TCP transfer

## Slide 4: Where does it come from? access networks, but not just access networks
Seen in serial lines, ISP DSH and optical networks at all speeds, LANs, WiFi networks, and input-queued backplanes such as Nexus – in fact, any queue
The buffering delay affects all traffic in the same or lower priority queue, particularly impacting delay sensitive applications like VOIP and rate-sensitive applications like video
Common reality to all of those:
  Offered load at an interface or on a path approximates or exceeds capacity, and as a result a queue builds, even if on a very short time scale
Shared media a special case:
  WiFi, single cable Ethernet, input-queued backplanes, and other shared media are best modeled as having two queues –
    One of packets in each interface
    One with interfaces seeking access to the channel
  As a result, in a congested shared medium, even an uncongested interface can experience congestion

## Slide 5: Fundamental Queuing theory
Average delay at an interface is inversely proportional to average available bandwidth
In other words, average delay shoots to infinity (loss) when a link is fully used.
  Independent of bandwidth (adding bandwidth changes or delays the effect, but does not solve the problem)
  Not driven by the number of sessions using the link (it might be a lot of little ones or a smaller number of big ones)
(M/M/1)
Graphic courtesy Sprint, Apricot 2004

## Slide 6: Not a new problem
Predicted by Kleinrock in 1960’s
  Dissertation and “Queueing Systems”
RFCs 896 and 970, dated 1984-1985, address network congestion
  TCP’s “Nagle” algorithm and the development of “fair” queuing
Subject of
  RFC 2309: Recommendations on Queue Management and Congestion Avoidance in the Internet.
  RFC 1633: Integrated Services in the Internet Architecture: an Overview
  RFC 2475: An Architecture for Differentiated Service.
  Extensive research, published in journals etc.
More recently:
  Jim Gettys et al, under the topic “bufferbloat” (ask Google)
But new ramifications…

## Slide 7: Growth of Video Traffic
Over coming years, expect video traffic – especially streaming media (video in TCP) – to dominate Internet traffic
Over-the-top providers including Netflix/Roku/Hulu,
video sites such as YouTube,
Video conferencing, Surveillance, etc
Composition of Video Traffic

## Slide 8: Service providers already struggling with service delivery in congested networks
Academic Research on non-responsive traffic flows
  “Router Mechanisms to Support End-to-End Congestion Control”
    ftp://ftp.ee.lbl.gov/papers/collapse.ps, Floyd & Fall
  “TCP-Friendly Unicast Rate-Based Flow Control”
    http://www.psc.edu/networking/papers/tcp_friendly.html, Floyd et al
Net Neutrality discussion
  “If you congest my network I’ll shut down your traffic!”
Comcast RFC 6057:
  Determine “top talker” subscribers from Netflow/IPFIX measurements
  Deprioritize or force round robin service
Fundamental issue:
  In each case, in various forms, a subscriber can impact SLA delivery for other subscribers. Solution: somehow throttle back the offending traffic flow.

## Slide 9: Parekh and Gallagher’s Proof
INFOCOMM ’93
If the objective is to have a predictable end to end delay through a network (which our applications would like to have)
One must have at most a predictable amount of traffic in the network
  TCP Window control, RTP Rate control, etc
One must have predictable traffic delay in each network element
  Which is mostly about queue depth
Given these, end-to-end delay of a host to host message is predictable
Notes: In 1993, a paper was published in INFOCOMM 1993, which was designed to put the controversy at rest. It asked the question “what points in the network must be predictable in order to make the network deliver a predictable round trip delay?” It consisted of a control-theoretic proof that decomposed the network into its parts and analyzed them.
The result, in hindsight, seems intuitively obvious, and will guide us in making our networks predictable for our applications. The network can deliver a predictable round trip delay to an application data stream if and only if two conditions hold:
  The application keeps a predictable amount of traffic in the network, and
  Each node en route does something predictable with that traffic.
“Each node” includes the originating host, the ultimate host, and the routers and switches that interconnect them. Some of our largest QoS problems are in the host operating systems themselves, so this is end to end in the most literal sense – application to application.

## Slide 10: Simple model of TCP throughput dynamics
Effective Window: the amount of data TCP sends each RTT
Knee: the lowest window that makes throughput approximate capacity
Cliff: the largest window that makes throughput approximate capacity
Note that throughput is the same at knee and cliff. Increasing the window merely increases RTT, by increasing queue depth
Increasing Measurable Throughput
Increasing TCP Window
“knee”
“cliff”
Bottleneck Capacity
Queue
Depth
Yes, there is a more complex equation that takes into account loss.
It estimates throughput above the cliff.

## Slide 11: TCP Congestion Control
Fundamental objective:
  To set and maintain the window at a point between the knee and the cliff, maximizing throughput for a given session
Possible secondary objectives:
  To be “fair” to competing sessions
  To be “unfair” to competing sessions
  To minimize loss
  To minimize startup or adaptation interval
  …
Depends on signals from the network to detect congestion!
  Delay-based congestion control detects onset of congestion, seeking some approximation to the knee. “Gentlemanly”
  Loss-based congestion control detects loss, approximating the cliff. Aggressive
  Explicit Congestion Notification detects network-initiated signals, seeking some approximation to the knee. Somewhere in between

## Slide 12: When the link utilization on a bottleneck link is below 90%, the 99th percentile of the hourly delay distributions remains below 1 ms. Once the bottleneck link reaches utilization levels above 90%, the variable delay shows a significant increase overall, and the 99th percentile reaches a few milliseconds. Even when the link utilization is relatively low (below 90%), sometimes a small number of packets may experience delay an order of magnitude larger than the 99th percentile”
“Analysis of Point-To-Point Packet Delay In an Operational Network”, INFOCOMM 2004, analyzing a 2.5 GBPS ISP network

## Slide 13: Issue: Signaling from the network
Many products provide deep queues and drop only from the tail when the queue is full
  That “1 ms” variation in delay can be in a queue producing a long delay, varying between 9 and 10 ms for example.
  The sessions affected most by tail drop are new sessions in slow-start, as they send relatively large bursts of traffic
  Occasional bursts result in unnecessary loss – unnecessarily poor service
Nick McKeown argues for very small total buffer sizes,
  Same net effect but a smaller average delay
  Defeats delay-based congestion control by reducing signal strength
Note, BTW, that lower rates imply longer intervals in queue
  In gigabit networks, we talk about single-digit milliseconds
  In megabit networks, we talk about tens to hundreds of milliseconds

## Slide 14: Tail Drop Traffic Timings
Mean Latency Correlates with Maximum Queue Depth
Typical variation
in delay only at
top of the queue

## Slide 15: The objective: generate signals early (RED, Blue, AVQ, AFD, etc)
Mean Latency Correlates with target queue depth, min-threshold
Additional Capacity to Absorb Bursts
Provide queues that can absorb bursts under normal loads, but which manage queues to a shallow average depth
Net effect: maximize throughput, minimize delay/loss, minimize SLA issues
Dynamic range of
configuration

## Slide 16: Three parts to the solution
Bandwidth, provisioning, and session control
  If you don’t have enough bandwidth for your applications, no amount of QoS technology is going to help. QoS technology manages the differing requirements of applications; it’s not magic.
  For inelastic applications – UDP and RTP-based sensors, voice, and video, this means some combination of provisioning, session counting, and signaling such as RSVP
Cooperation between network and host mechanisms for elastic traffic
  Parekh and Gallagher
  TCP Congestion Control responds to signals from the network or measurements of the network
Choices in network signaling
  Loss – TCP responds to loss
  Explicit Congestion Notification – lossless signaling from the network

## Slide 17: Avoiding loss: RFC 3168 Explicit Congestion Notification
Manage congestion without loss
When AQM would otherwise drop traffic to signal queue deeper than some threshold, mark it “Congestion Experienced”
TCP Receiver reports back to sender, who reduces window accordingly
TCP
IP
IP
TCP
IP
negotiation
Notes: A recently published standard provides the way to accomplish that. It is called Explicit Congestion Notification.
In this procedure, TCP uses two previously-unused bits to negotiate between peers. If two communicating peers both support the procedure, they use the two remaining bits in the TOS byte to discuss congestion.
There are two bits: “I understand ECN” and “this packet experienced congestion.” The TCP peers set “I understand ECN” on all traffic in that exchange. Should RED or WRED decide to randomly mark a packet, instead of dropping it, they mark it as having “experienced congestion.”
The receiving TCP uses the same bits in the TCP header to advise the sender to reduce his effective window. Net effect: throughput rate is temporarily reduced to match bottleneck, but TCP session continues instead of waiting for a time-out.
In long-lived sessions, goodput rate improves due to elimination of timeouts.
In short-lived sessions, goodput rates improved as well.

## Slide 18: Some recommendations

## Slide 19: In data centers and content networks: Delay-based TCP Congestion Control
In our dreams, hosts would implement a delay-based TCP
  By seeking an approximation to the knee, maximizes throughput while minimizing impact on competing traffic
CalTech FAST
  Seeks to keep a quantum in the bottleneck queue
  Adapts more rapidly than traditional congestion control
  Effective, but doesn’t compete well with loss-based algorithms
Hamilton Institute Delay-based Algorithm
  Seeks to keep bottleneck queue statistically empty
  Competes well with loss-based algorithms
Swinburne CAIA Delay-based Algorithm
  Seeks to keep bottleneck queue statistically empty
  Competes well with loss-based algorithms

## Slide 20: Mark-based TCP
Explicit Congestion Control
RFC 3168 ECN:
  On receipt of ECN Congestion Experienced, return signal in TCP to sender
  Sender reduces effective window by the same algorithm it uses on detection of loss
Data Center TCP (DCTCP):
  Based on RFC 3168 (responds either to loss or ECN marks)
  Reduces effective window proportionally to mark rate

## Slide 21: And in your network…
Routing and switching products should:
  Implement an AQM algorithm (RED, AVQ, Blue, etc.) on all interfaces
  Implement both dropping and ECN marking
Target queue depth (informal recommendation):
Bit rate (order of magnitude) | Min-thresh (ms) | Max-thresh (ms) | Target Packets in queue
104 | 2400 | 6000 | 2
105 | 240 | 2400 | 2
106 | 32 | 320 | 2.6
107 | 16 | 160 | 13
108 | 8 | 80 | 67
109 | 4 | 40 | 333
1010 | 2 | 20 | 1667
1011 | 1 | 10 | 8333